## Slide 1
Elena Perevedentseva1, Elena Muronets2, Artashes Karmenyan3, Chia-Liang Cheng3,
Irina Elanskaya2, Nikolai Melnik1
1 P.N. Lebedev Physical Institute Rus. Acad. Sci., Moscow, Russia 2 Biological Dept of Moscow State University, Moscow, Russia 3 Department of Physics, National Dong Hwa University, Hualien, Taiwan
perevedencevaev@lebedev.ru
ANNUAL INTERNATIONAL CONFERENCE
SARATOV FALL MEETING XXVI
26-30 September, 2022, Saratov, Russia
Raman spectroscopic investigations of functional state of unicellular organisms

## Slide 2
1. Motivation
2. Introduction:
2.1. Methods
2.2. Studies on detection and identifying, characterization of microbial virulence factors, accessing the pathogenic microorganism’s sensitivity to treatment and drug effects monitoring, the effects of stressor factors
2.3. Laser as stressor factor, safety of Raman measurements
2.4. Probing of microorganism s’ molecular species and analyzing physiological state/processes and metabolic reactions; using microorganism as a model for study of physiological processes
3. Raman study of pathogenic bacteria response (for a gram-negative E. coli) to treatment with detonation nanodiamond
4. Raman study of Amoeba (Acanthamoeba polyphaga) life cycle: cyst activation and excystaion processes
5. Raman spectroscopy of phycobiliproteins deficiency in cyanobacteria Synechocystis sp. PCC 6803 mutants
6. Conclusion
Outline

## Slide 3
Raman spectroscopy on microorganisms:
Detection and identifying pathogenic or non-pathogenic microorganisms.
2. Probing of microorganisms molecular species and analyzing physiological state/processes and metabolic reactions
for characterization of microbial virulence factors
for drug effects monitoring and accessing the pathogenic microorganism’s sensitivity to treatment, e.g. bacterium’s sensitivity to antibiotic, alcohol, other stress factors
ecological studies and monitoring; testing the ecological role of the microorganisms
3. Using the fact that microorganism can serve as a good model of higher organisms in studies of some physiological processes
Motivation

## Slide 4
Conventional Raman spectroscopy;
Surface Enhanced Raman Spectroscopy (SERS);
Coherent Raman Spectroscopy (CRS ) – Stimulated Raman Spectroscopy (SRS) and Coherent Anti-Stocks Raman Spectroscopy (CARS);
Raman with Laser Tweezers
+ new statistical methods and machine learning
introduction
W. Zhang et al 2022, https://doi.org/10.3390/photonics9030133

## Slide 5
W. Zhang et al, A Review of Raman-Based Technologies for Bacterial Identification and Antimicrobial Susceptibility Testing Photonics 9(3), 133, 2022.
Rebrošová, K et al, Raman Spectroscopy—A Novel Method for Identification and Characterization of Microbes on a Single-Cell Level in Clinical Settings. Front. Cell. Infect. Microbiol., Sec. Clinical Microbiology, 2022 https://doi.org/10.3389/fcimb.2022.866463.
Almarashi, J. F. M. et al. Raman Spectroscopy of Bacterial Species and Strains Cultivated Under Reproducible Conditions. Spectroscopy: Int. J. 27, 361, 2012.
Maquelin, K., et al. Prospective Study of the Performance of Vibrational Spectroscopies for Rapid Identification of Bacterial and Fungal Pathogens Recovered From Blood Cultures. J. Clin. Microbiol. 41 (1), 324, 2003
Rebrošová, K. et al. Identification of Ability to Form Biofilm in Candida Parapsilosis and Staphylococcus Epidermidis by Raman Spectroscopy. Future Microbiol. 14 (6), 509, 2019
introduction
Detection and identifying

## Slide 6
Drug monitoring and antibiotic susceptibility testing
Neugebauer, U et al. Raman Spectroscopy Towards Clinical Application: Drug Monitoring and Pathogen Identification. Int. J. Antimicrob. Agents 46, S35, 2015
Nakar, A.,et al. Detection of Multi-Resistant Clinical Strains of E. Coli With Raman Spectroscopy. Anal. Bioanal. Chem. 18, 1481, 2022
T.-T. Liu et al. A High Speed Detection Platform Based on Surface Enhanced Raman Scattering for Monitoring Antibiotic Induced Chemical Changes in Bacteria Cell Wall. PLoS ONE 4(5): e5470 2009
Rousseau, A. N. et al. (2021). Fast Antibiotic Susceptibility Testing via Raman Microspectrometry on Single Bacteria: An MRSA Case Study. ACS Omega 6 (25), 16273, 2021
Mathey, R et al. Viability of 3h Grown Bacterial Micro-Colonies After Direct Raman Identification. J. Microbiol Methods 109, 67, 2015.
introduction

## Slide 7
Staphylococcus epidermidis
Escherichia coli
Raman measurements safety
S. epidermidis (I) and E. coli (II) micro-colonies were exposed to Raman laser and BacLight stained. For each species, laser beam was visualized on a microcolony panel in reflection microscopy. Corresponding images of compiled envelope integrity markers Syto 9 and Propidium Iodide fluorescence are presented . Scale bars= 25 μm
(I)
(II)
Excitation with 532 nm laser, 120 sec exposure, laser power at the sample – 36 mW
introduction
R. Mathey et al, 2015. J. Microbiol Methods 109, 67–73. doi: 10.1016/j.mimet.2014.12.002

## Slide 8
Budding yeast (Saccharomyces cerevisiae, Schizosaccharomyces pombe) are considered as simplest unicellular eukaryote whose cell cycle has many features in common with those of higher eukaryotes
The Raman spectroscopic signature of life is band at 1602 cm-1 that sharply reflects the metabolic activity of cell (yeast) mitochondria.
Microorganism as a model to study physiological processes
A molecular imaging method was developed based on Raman mapping + multivariate data analyses such as principal component analysis (PCA), cluster analysis and multivariate curve resolution (MCR) –
to elucidate the molecular compositions of organelles
of the yeast starting its budding
Noothalapati, H. et al. Label-free Chemical Imaging of Fungal Spore Walls by Raman Microscopy and Multivariate Curve Resolution Analysis. Sci Rep 6, 27789, 2016
L.D. Chiu et al, (2010). J Raman Spectroscopy 41(1), 2, 2010
Naito Y et al, J Raman Spectrosc. 36: 837, 2005
Y S Huang et al, Biochemistry 44, 10009, 2005
introduction

## Slide 9
(a) Optical image of a single E. coli interacted with DND aggregate
(b) Raman mapping in the 1000 to 3000 cm−1 wavenumber region obtained with a 488 nm laser excitation and at 6 mW laser power at the 100× (NA 0.90) objective output.
Raman spectroscopy and mapping
(c) Raman spectra from DND (revealing the lines in 1290-1370 cm−1 range from sp2-sp3 Carbon) attached at the bacterial cell membrane measured in point 1 marked in (b) and for E. coli corresponding to point 2 marked in (b) with pronounced Raman signal attributed to C-H bonds (2820 - 3030 cm−1)
(a)
(b)
Interaction of E. coli with DND (25 μg∕ml)
for 30 s in aqueous medium
Raman study of pathogenic bacteria (gram-negative E. coli) response to treatment with detonation nanodiamond (DND)
A. Chatterjee, E. Perevedentseva, M. Jani, C.-Y. Cheng, Y.-S. Ye, P.-H. Chung, C.-L. Cheng. Antibacterial effect of ultrafine nanodiamond against gram-negative bacteria Escherichia coli. J Biomed Opt 20(5), 051014, 2015; doi: 10.1117/1.JBO.20.5.051014

## Slide 10
Raman spectra of a single untreated E. coli (control) and E. coli treated with 5 nm DND (25 μg∕ml) measured at different points (marked) of the bacterial cell wall surface. The inset shows the Raman mapping of the single E. coli treated with DND
Raman study of pathogenic bacteria (gram-negative E. coli) response to treatment with detonation nanodiamond (DND)
A. Chatterjee, E. Perevedentseva, M. Jani, C.-Y. Cheng, Y.-S. Ye, P.-H. Chung, C.-L. Cheng. Antibacterial effect of ultrafine nanodiamond against gram-negative bacteria Escherichia coli. J Biomed Opt 20(5), 051014, 2015; doi: 10.1117/1.JBO.20.5.051014
1654 cm−1
1667 cm−1

## Slide 11
Amoeba (trophozoite) encystation under the temperature decreasing to 4°C
Amoeba cyst activation and following excystation
after normalizing environmental conditions and nutrients
Raman study of Amoeba (Acanthamoeba polyphaga) life cycle: cyst activation and excystaion processes
Y.C. Lin, E. Perevedentseva, C.L. Cheng: Raman spectroscopic study on the excystation process in a single unicellular organism amoeba (Acanthamoeba polyphaga). J Biomed Optics 20(5), 051042, 2015

## Slide 12
Mature cyst transformation to activated cyst stage: (I) Raman spectra of mature cyst transforming to activated cyst stage. The spectra intensities are normalized to
1007 cm−1 band. (II) Dependences of Raman peaks intensity on time at cyst activation.
Excitation 488 nm, laser power at the sample 0.1 mW
(II)
(I)
Raman shift, cm-1
Raman study of Amoeba (Acanthamoeba polyphaga) life cycle: cyst activation and excystaion processes
3025 cm-1
1519 cm-1
Y.C. Lin, E. Perevedentseva, C.L. Cheng: Raman spectroscopic study on the excystation process in a single unicellular organism amoeba (Acanthamoeba polyphaga). J Biomed Optics 20(5), 051042, 2015

## Slide 13
Raman shift, cm-1
Raman study of Amoeba (Acanthamoeba polyphaga) life cycle: laser treatment
Y.C. Lin, E. Perevedentseva, C.L. Cheng: Raman spectroscopic study on the excystation process in a single unicellular organism amoeba (Acanthamoeba polyphaga). J Biomed Optics 20(5), 051042, 2015

## Slide 14
(a) cultured cyanobacteria Synechocystis of wild type (WT), CK mutant, and PAL mutant ; (b) corresponding microscopic images of the cells in medium
WT CK PAL
WT
CK
PAL
(a) (b)
Raman spectroscopy of phycobiliproteins deficiency in cyanobacterium Synechocystis mutants

## Slide 15
Raman spectroscopy of phycobiliproteins deficiency in cyanobacterium Synechocystis mutants
PSII
Thylakoid membrane
(A)
(B)
(C)
Phycobilisome and PSII in cyanobacteria; a, b, c units are organized by 4 molecules of allophycocyanin; d, e, f, g units are organized by 3 molecules of phycocyanin:
(A) – WT, (B) – CK, (C) - PAL
PSII
Phycobilisome
Thylakoid membrane
A
B
C
PSII
Thylakoid membrane
Phycobilisome

## Slide 16
Excitation 785 nm
Laser power 50 mW
at the sample
Excitation 1064 nm
Power 175 mW
These 3 types reveal differences (in the areas, marked by arrows) in Raman-active species attributed* to Phycobiliproteins - water-soluble proteins forming light harvesting antenna (phycobilisome) for photosystem II (PSII, photosynthesis complex in plants, algae and cyanobacteria).
*in accordance to P. Vitek, J. Wierzchos 2020, in Desert biosignatures, Springer
Raman spectra of wild type of Synechocystis (WT), CK mutant, and PAL mutant measured at excitations 785 nm (a) and 1064 nm (b).
Raman spectroscopy of phycobiliproteins deficiency in cyanobacterium Synechocystis mutants

## Slide 17
On the example of various microorganisms we confirmed Raman applications for the microorganism s detection , for analysis their conditions and for study their functioning on biomolecular level.
conclusion
Thank you for your attention!